elua Manual

v 0.00.01
Changelog:

2008 Nov, 30:
   The present version of the eLua Manual is basically an assembly of the previous .txt documents.
   Initial documentation for The "disp" module, with support for the OLED RIT128x96x4 display on the LM3S8962 Luminary Board was added.

eLua components
=====================================================================

Besides the Lua core, the platform modules (docs/platform_modules.txt) and the
Newlib 'glue code', eLua uses a number of other code modules (components) for
extended functionality. This is a great thing if you actually need the whole
functionality in your code, but otherwise it becomes a waste of memory space.
Since eLua was designed to be as flexible as possible, it includes a mechanism
that allows the user to select exactly what components he needs. Only the
selected components will be part of the eLua image. Please note that this is
_not_ a replacement of the platform modules mechanism, the two are complementary
to each other, since the components are not connected with the platform
interface (docs/platform_interface.txt) in any way.
To use this feature, every platform (src/platform/[name]) must include a file
named "platform_conf.h" that specifies (among other things) what components
should be built for that platform. For example, the LM3S "platform_conf.h" file
might look like this:

(BEGIN src/platform/lm3s/platform_conf.h)
// Define here what components you want for this platform

#ifndef __PLATFORM_CONF_H__
#define __PLATFORM_CONF_H__

#define BUILD_XMODEM
#define BUILD_SHELL
#define BUILD_ROMFS
#define BUILD_TERM
........................................
(END src/platform/lm3s/platform_conf.h)

In this case, the XMODEM, SHELL, ROMFS and TERM components will be built. On the
other hand, the i386 "platform_conf.h" will probably have less components:

(BEGIN src/platform/i386/platform_conf.h)
// Define here what components you want for this platform

#ifndef __PLATFORM_CONF_H__
#define __PLATFORM_CONF_H__

#define BUILD_ROMFS
#define BUILD_SHELL
........................................
(END src/platform/i386/platform_conf.h)

You don't need to modify any other part of your code, just rebuild your image
after you made changes to this file (docs/building.txt)
Below you can find a list of eLua components and their functionality.

XMODEM
=====================================================================
The XMODEM component enables eLua to receive Lua source files via its shell and
execute them (docs/the_elua_shell.txt). If you don't need to use "recv" from the
shell you can skip this component.
To enable:
  #define BUILD_XMODEM

Also, XMODEM is configured with a number of constants also defined in
platform_conf.h. They are:

XMODEM_UART_ID : the id of the UART on which XMODEM runs
XMODEM_TIMER_ID : the id of the timer used by the XMODEM implementation

SHELL
=====================================================================
This enables the build of the eLua shell (docs/the_elua_shell.txt). If you don't
need the shell, don't enable this component. eLua will execute the "lua" command
at startup if the eLua shell is not built. The shell comes in two flavours: over
a serial line or over TCP/IP (currently you can't have both at the same time).
To enable shell over a serial line:
  #define BUILD_SHELL
  #define BUILD_CON_GENERIC
To enable shell over TCP/IP:
  #define BUILD_SHELL
  #define BUILD_CON_TCP

ROMFS
=====================================================================
If you need to use the ROM file system (docs/the_rom_file_system.txt) enable
this component, otherwise you can skip it.
To enable:
  #define BUILD_ROMFS

TERM
=====================================================================
The TERM module adds support for ANSI terminals. See docs/terminal_support.txt
for details. If you don't need it, and if you're willing to miss the opportunity
of playing hangman in eLua (examples/hangman.lua) you can skip this component :)
To enable:
  #define BUILD_TERM

Also, TERM is configured with a number of constants also defined in
platform_conf.h. THey are:

TERM_UART_ID - the id of the UART on which TERM runs
TERM_TIMER_ID - the id of the timer used by the TERM implementation
TERM_LINES - number of lines in the terminal emulator
TERM_COLS - number of columns in the terminal emulator
TERM_TIMEOUT - inter-key timeout (used to detect keys that send multiple codes,
  such as up/down/left/right keys).

IMPORTANT NOTE: TERM doesn't currently work over TCP/IP.

uIP
=====================================================================
uIP is the TCP/IP stack used curently by eLua to provide networking support
(docs/tcpip_in_elua.txt). You can enable the TCP/IP stack and two of its services
(the DHCP client and the DNS resolver).
To enable uIP (thus TCP/IP support):
  #define BUILD_UIP
To enable the DHCP client:
  #define BUILD_DHCPC
To enable the DNS resolver:
  #define BUILD_DNS
eLua generic modules
=====================================================================

Before you read this file, please make sure that you read and understood the
theory from "platform_modules.txt" (at least the first part which describes
the platform modules implementation). The generic modules use the exact same
mechanism. In fact, the only difference between them is that the generic modules
are exactly what their name implies: generic. They don't depend on the platform
interface, so they don't need specific support for each platform, but they still
behave identically on all platforms. They are selected by the same mechanism
used by the platform modules (platform_libs.h). Following is a list of these
modules and their exported functions.

The "term" module
=====================================================================
The "term" component (see terminal_support.txt) exports its functions to Lua via
the "term" module. The methods of the "term" module are presented below.

term.clrscr(): clear the screen

term.clreol(): clear from the current cursor position to the end of the line

term.gotoxy( x, y ): position the cursor at the given coordinates

term.up( delta ): move the cursor up "delta" lines

term.down( delta ): move the cursor down "delta" lines

term.left( delta ): move the cursor left "delta" lines

term.right( delta ): move the cursor right "delta" lines

Lines = term.lines(): returns the number of lines

Cols = term.cols(): returns the number of columns

term.put( c1, c2, ... ): writes the specified character(s) to the terminal

term.putstr( s1, s2, ... ): writes the specified string(s) to the terminal

Cx = term.cursorx(): return the cursor X position

Cy = term.cursory(): return the cursor Y position

c = term.getch( term.WAIT | term.NOWAIT ): returns a char read from the
  terminal. If term.WAIT is specified the function will wait for a character to
  be ready, with term.NOWAIT it returns -1 if no char is available or the char
  code if a char is available. The return of getch can be checked against the
  char codes defined in inc/term.h, by appending "term." to the constant name
  (for example: term.KC_UP, term.KC_LEFT, term.KC_ESC ... )

The "pack" module
=====================================================================
Pack allows packing/unpacking of binary data. For example, it allows one to save
a specific data type (for example a 16-bit integer) from Lua to a file and then
read it back to a Lua variable without having to worry about the different
physical representations of a Lua number and a 16-bit integer. It's originally
written by Luiz Henrique de Figueiredo, one of the "fathers" of Lua.
It exports just two methods ("pack" and "unpack"), but it uses some format
specifiers for the pack/unpack operations that take a while to get used to. For
more information download the original distribution and check its documentation
and examples (http://www.tecgraf.pub-rio.br/~lhf/ftp/lua/~lpack).

The "bit" module
=====================================================================
As Lua doesn't have built-in operators for bit operations (and, or, xor, not)
they are provided by this module. It's based on "bitlib" by Reuben Thomas and
was slightly adapted and augmented for eLua.

Res = bit.bnot( value ): unary negation

Res = bit.band( v1, v2, ... ): binary "and"

Res = bit.bor( v1, v2, ... ): binary "or"

Res = bit.bxor( v1, v2, ... ): binary "exclusive or"

Res = bit.lshift( value, pos ): shift "value" left "pos" positions.

Res = bit.rshift( value, pos ): shift "value" right "pos" positions. The sign is
  not propagated.

Res = bit.arshift( value, pos ): shift "value" right "pos" positions. The sign
  is propagated ("arithmetic shift").

Res = bit.bit( bitno ): a shortcut for bit.lshift( 1, bitno )

Res1, Res2, ... = bit.set( bitno, v1, v2, ... ): set the bit at position "bitno"
  in v1, v2, ... to 1.

Res1, Res2, ... = bit.clear( bitno, v1, v2, ... ): set the bit at position
  "bitno"in v1, v2, ... to 0.

Res = bit.isset( value, bitno ): returns true if bit at position "bitno" in
  "value" is 1, false otherwise.

Res = bit.isclear( value, bitno ): returns true if bit at position "bitno" in
  "value" is 0, false otherwise.

The "math" module
=====================================================================
This is actually part of the official Lua distribution, not a separate module.
Its purpose is to provide mathematic functiosn (sin, cos, tan...) to Lua. Since
these kind of functions are rarely needed in an embedded environment, the "math"
module can be enabled and disabled just like the other generic and platform
modules in eLua.

The "net" module
=====================================================================
TCP/IP networking support is provided to eLua via the "net" module. It contains
a small set of function, tailored for embedded systems (lighter and less resource
demanding).

IMPORTANT NOTE: TCP/IP support in eLua is still largely experimental.

Sock = socket( type ): creates a new socket and returns its identifier. type can
be either net.SOCK_STREAM or net.SOCK_DGRAM, but currently only TCP/IP sockets
(SOCK_STREAM) are implemented.

Res = close( socket ): closes the given socket, returning an error status.

IP = packip( ip0, ip1, ip2, ip3 ) or IP = packip( "ipstring" ): packs the given
IP (either in unpacked form or as a string) returning a value that completely
identifies that IP (it's not actually a new IP datatype, just a 32-bit number).

IP0, IP1, IP2, IP3 = unpackip( ip, "*n" ) or IPString = unpackip( ip, "*s" ):
unpacks the given IP value, returning it either as 4 numbers or as a string.

Sock, RemoteIp, Err = accept( port, [timer_id, timeout] ): listens on the
specified port, waiting for connections. If timer ID and timeout are specified,
it uses the specified timer to wait for a connection for at most "timeout"
microseconds. Returns the socket descriptor for the new connection, the IP of
the remote end, and an error status.

Sent, Res = send( sock, string ): send the given "string" on the specified
socket, returning the number of bytes actually send and an error status.

Data, Res = recv( sock, maxsize, [timer_id, timeout] ) or
Data, Res = recv( sock, "*l", [timer_id, timeout] ): read data from the
socket. The first form reads up to a maximum size specified by "maxsize", the
second form reads a single line (until '\n' is received, ignoring any '\r'
chars in the stream).
IMPORTANT NOTE: currently, the "*l" (line) mode is partially broken, in that it
might loose some of the data sent by the remote end. If the remote end sends
more than one line, only the first is kept, the rest is ignored. For example,
if the remote sends "line\n", everything is OK, but if the remote sends
"line1\nline2\n", "line1" is returned correctly after calling "recv" once, but
"line2" won't be returned after calling "recv" again. This is due to the "single
buffer" design of uIP. If you want to make sure you receive all the data you're
looking for, use the first form of recv, specifying a maximum size. "*l" is only
usable for line-oriented conversations (like you'd find in a command line shell,
for example).

IP = lookup( "hostname" ): invokes the DNS resolver to find the IP address of
"hostname".

Err = connect( sock, ip, port ): connects the specified socket (that must be
created previously using "socket") to the specified host and port. Returns an
error status.

The error status is defined in inc/elua_net.h in one enum:

(BEGIN inc/elua_net.h)
// eLua net error codes
enum
{
  ELUA_NET_ERR_OK = 0,
  ELUA_NET_ERR_TIMEDOUT,
  ELUA_NET_ERR_CLOSED,
  ELUA_NET_ERR_ABORTED,
  ELUA_NET_ERR_OVERFLOW
};
(END inc/elua_net.h)
The "disp" module
  The disp module provides support for graphical displays.
  This documentation is somewhat focused on the single display supported so far.

Platforms supported: LM3S8962
Displays supported: RIT Oled display RIT128x96x4

Module functions:

disp.init( freq )
  This function initializes the SSI interface to the OLED display and

configures the SSD1329 controller on the panel.

Parameters:
  freq: specifies the SSI Clock Frequency to be used.

disp.enable( freq )
  This function initializes the SSI interface to the OLED display

Parameters:
  freq: specifies the SSI Clock Frequency to be used.

disp.disable()
  This function frees the SSI interface to be used to some other function.

Parameters:
  None.

disp.on()
  This function will turn on the OLED display, causing it to display the
 contents of its internal frame buffer.

Parameters:
  None.

disp.off()
  This function will turn off the OLED display. This will stop the scanning
 of the panel and turn off the on-chip DC-DC converter, preventing damage to
 the panel due to burn-in (it has similar characters to a CRT in this
 respect).

Parameters:
  None.

disp.stringdraw(str, x, y, lvl)
  This function prints a string on the an x, y pixel position on the graphical display.

Parameters:
  str: string to be printed
  x: screen column position in pixels (0-127)
  y: screen line position in pixels (0-95)
  lvl: intensity level / gray level (0-15)

Obs:
  Only the ASCII characters
 between 32 (space) and 126 (tilde) are supported. Other characters will
 result in random data being draw on the display.
  If the drawing of the string reaches the right edge of the display, no more
 characters will be drawn. Therefore, special care is not required to avoid
 supplying a string that is too long to display.
  Because the OLED display packs 2 pixels of data in a single byte, the
 parameter x must be an even column number.

disp.imagedraw(img, x, y, w, h)
  This function will display a bitmap graphic on the display.

Parameters:
  img: image stream to be printed
  x: screen column position in pixels (0-127)
  y: screen line position in pixels (0-95)
  w, h: image width and height dimensions

Obs:
  Because of the
 format of the display RAM, the starting column (x) and the number of
 columns (w) must be an integer multiple of two.

  The image data is organized with the first row of image data appearing left
 to right, followed immediately by the second row of image data. Each byte
 contains the data for two columns in the current row, with the leftmost
 column being contained in bits 7:4 and the rightmost column being contained
 in bits 3:0.

  For example, an image six columns wide and seven scan lines tall would
 be arranged as follows (showing how the twenty one bytes of the image would
 appear on the display):

+-------------------+-------------------+-------------------+

| Byte 0 | Byte 1 | Byte 2 |

+---------+---------+---------+---------+---------+---------+

| 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 |

+---------+---------+---------+---------+---------+---------+

| Byte 3 | Byte 4 | Byte 5 |

+---------+---------+---------+---------+---------+---------+

| 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 |

+---------+---------+---------+---------+---------+---------+

| Byte 6 | Byte 7 | Byte 8 |

+---------+---------+---------+---------+---------+---------+

| 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 |

+---------+---------+---------+---------+---------+---------+

| Byte 9 | Byte 10 | Byte 11 |

+---------+---------+---------+---------+---------+---------+

| 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 |

+---------+---------+---------+---------+---------+---------+

| Byte 12 | Byte 13 | Byte 14 |

+---------+---------+---------+---------+---------+---------+

| 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 | 7 6 5 4 | 3 2 1 0 |

+---------+---------+---------+---------+---------+---------+

Console input/output in eLua
=====================================================================

NOTE: this document describes the terminal support over serial connections
only. Refer to docs/elua_components.txt to learn how to enable console
support over TCP/IP instead of serial connections.

The console input/output is handled by a generic layer (src/newlib/genstd.c)
that can be adapted to a variety of input/output devices. It needs just two
functions, one for displaying characters and another one for receiving input:

(BEGIN inc/newlib/genstd.h)
// Send/receive function types
typedef void ( *p_std_send_char )( int fd, char c );
typedef int ( *p_std_get_char )();
(END inc/newlib/genstd.h)

(the send faction gets an additional 'fd' parameter that you can use to
differentiate between STDOUT and STDERR).
To set them, use std_set_send_func and std_set_get_func. Generally this happens
in the "platform_init" function (see "platform interface.txt") to set the
initial "console" device:

(BEGIN src/platform/at91sam7x/platform.c)
int platform_init()
{
.........................
  // Set the send/recv functions
  std_set_send_func( uart_send );
  std_set_get_func( uart_recv );
.........................
}
(END src/platform/at91sam7x/platform.c)

The code above makes it possible for you to use the UART as the Lua console,
thus being able to use the standard Lua interpreter (for example) via your
serial connection.
If you need another console device, just call std_set_send_func/std_set_get_func
with the appropriate function pointer.

eLua platform interface
=====================================================================
This document describes the "platform" interface in eLua. Its purpose is to ease
the task of porting eLua to a new platform, as well as having a uniform layer
for accesing peripherals (such as PIO, UART, SPI ...) on all platforms.

The definitions of the functions shown here are in the "inc/platform.h" file.
Some of the functions are required, others are optional; see also the "adding
a new platform.txt" and "platform modules.txt" files for additional information.
Also, for each function or function group, the name of the module(s) that use
it (if any) is specified. If other part of the code uses the module, a
"ALSO USED BY" line will be present in the module description.

============================================================================

int platform_init();

TYPE: REQUIRED
USED BY MODULE: N/A

PURPOSE: platform-specific initialization (this is a good place to initialize
the platform CPU, as well as the CPU peripherals, like the UART).
RETURNS: PLATFORM_OK or PLATFORM_ERR (if PLATFORM_ERR is returned the program
blocks in an infinite loop).

============================================================================

void* platform_get_first_free_ram( unsigned id );
void* platform_get_last_free_ram( unsigned id );

TYPE: REQUIRED
USED BY MODULE: N/A

PURPOSE: returns the first and the last free RAM address; the space between them
will be used for the system heap. 'id' is a memory space identifier. This can be
used if there is more than one RAM memory available in the system, and their
address ranges do not overlap. For example, one can have a CPU with internal RAM
(a very common case) but also an external RAM chip. In this case there are two
memory spaces, the first one being the internal RAM and the other one the
external RAM. While each of them in part is contiguous, they are generally not
contigous to each other in the system address space, so they must be treated as
two separate address spaces. If the multiple allocator (see building.txt) is
used you can define as many memory spaces as you wish in your system, the
allocator will make sure to use all of them.
If the system RAM exists in a single memory space (for example the internal RAM
on the MCU) the CPU's stack pointer should be set at the end of the RAM at
startup. Thus, the first free ram will start right after the data/bss sections,
and the last free RAM is the last physical address of RAM minus the size of the
stack. The heap and the stack will grow on opposite directions (upward/downward)
and the heap will stop if asked to grow "over" the stack.
If the MCU has both internal RAM and external RAM, a simple arrangement is to
place the CPU stack at the end of the internal RAM and the heap in the external
memory (which is generally much larger than the MCU's internal memory). Another
arrangement is to use the multiple allocator and the memory space id as
described above.

=====================================================================int platform_pio_has_port( unsigned port );
const char* platform_pio_get_prefix( unsigned port );
int platform_pio_has_pin( unsigned port, unsigned pin );
pio_type platform_pio_op( unsigned port, pio_type pinmask, int op );

TYPE: OPTIONAL
USED BY MODULE: pio

PURPOSE: PIO operations. eLua defines a number of "virtual ports", each one 32
bits in size, as shows in "inc/platform.h". But since it somehow needs to map
these virtual ports to physical ports, it will ask the platform if a port is
physically present (via platform_pio_has_port) and also if a bit (a "pin") in
the port is physically present (via platform_pio_has_pin).
platform_pio_get_prefix gets a port number and return the "port name" as defined
in the device datasheet. Some devices use PA0, PA1, others simply P0, P1. This
is what this function is expected to return.
The platform_pio_op function is the one that does the actual work with the PIO
subsystem. It receives an operation id ("op") as well as a mask ("pinmask") to
which the operation applies. The possible operations are shown in the 'enum'
below (taken from "inc/platform.h"):

(BEGIN inc/platform.h)
enum
{
  // Pin operations
  PLATFORM_IO_PIN_SET, // Set pin(s) to 1
  PLATFORM_IO_PIN_CLEAR, // Set pin(s) to 0
  PLATFORM_IO_PIN_GET, // Get value of pin
  PLATFORM_IO_PIN_DIR_INPUT, // Configure pin(s) as input
  PLATFORM_IO_PIN_DIR_OUTPUT, // Configure pin(s) as output
  PLATFORM_IO_PIN_PULLUP, // Enable pullups on the pin(s)
  PLATFORM_IO_PIN_PULLDOWN, // Enable pulldowns on the pin(s)
  PLATFORM_IO_PIN_NOPULL, // Disable all pulls on the pin(s)
  // Port operations
  PLATFORM_IO_PORT_SET_VALUE, // Set port value
  PLATFORM_IO_PORT_GET_VALUE, // Get port value
  PLATFORM_IO_PORT_DIR_INPUT, // Configure port as input
  PLATFORM_IO_PORT_DIR_OUTPUT // Configure port as output
};
(END inc/platform.h)

=====================================================================
int platform_spi_exists( unsigned id );
u32 platform_spi_setup( unsigned id, int mode, u32 clock, unsigned cpol,
        unsigned cpha, unsigned databits );
spi_data_type platform_spi_send_recv( unsigned id, spi_data_type data );
void platform_spi_select( unsigned id, int is_select );

TYPE: OPTIONAL
USED BY MODULE: spi

PURPOSE: SPI operations. eLua defines 4 "virtual" SPI interfaces. The function
platform_spi_exists() gets an identifier from 0 to 3 and returns 1 if the SPI
interface with the given identifier exists on the target machine, 0 ohterwise.
platform_spi_setup() is called to configure the SPI interface with the given
parameters, returning the actual clock that was set for the interface. The
actual data transfer is done by calling platform_spi_send_recv(), which executes
a SPI "cycle" (send one byte, receive one byte). Finally, platform_spi_select()
is used to set the state of the SPI SS (slave select) pin, if the target's SPI
interface provides this functionality.

=====================================================================

int platform_uart_exists( unsigned id );
u32 platform_uart_setup( unsigned id, u32 baud, int databits, int parity,
        int stopbits );
void platform_uart_send( unsigned id, u8 data );
int platform_uart_recv( unsigned id, unsigned timer_id, int timeout );

TYPE: OPTIONAL
USED BY MODULE: uart
ALSO USED BY: XMODEM, TERM over UART

PURPOSE: UART operations. eLua defines 4 "virtual" UART interfaces. The function
platform_uart_exists() gets an identifier from 0 to 3 and returns 1 if the UART
interface with the given identifier exists on the target machine, 0 ohterwise.
platform_uart_setup() is called to configure the SPI interface with the given
parameters, returning the actual baud that was set for the interface. The
actual data transfer is done by calling platform_uart_send to send a byte, and
platform_uart_recv to receive a byte. The receive function has a timeout than
can take different values:

- timeout == 0: receive without waiting for data. If a data byte is available
  return it, otherwise return -1.
- timeout == PLATFORM_UART_INFINITE_TIMEOUT: wait until a data byte is available
  and then return it. This will block indefinetely if no data is available.
- timeout > 0: if a data byte is available in the give time (expressed in us)
  return id, otherwise return -1.

=====================================================================

int platform_timer_exists( unsigned id );
void platform_timer_delay( unsigned id, u32 delay_us );
u32 platform_timer_op( unsigned id, int op, u32 data );
u32 platform_timer_get_diff_us( unsigned id, timer_data_type end,
        timer_data_type start );

TYPE: OPTIONAL
USED BY MODULE: tmr, uart (for receive with timeout)
ALSO USED BY: XMODEM, TERM over UART

PURPOSE: timer operations. eLua defines 16 "virtual" timers. The function
platform_timer_exists() gets an identifier from 0 to 15 and returns 1 if the
timer with the given identifier exists on the target machine, 0 otherwise.
platform_timer_delay() will block the execution for the specified number of
microseconds, and platform_timer_get_diff_us() gets two timer values and returns
the time difference (in microseconds) between them.
platform_timer_op() executes the specified operation on the givem timer. The
operations are defined in an enum from inc/platform.h:

(BEGIN inc/platform.h)
// Timer operations
enum
{
  PLATFORM_TIMER_OP_START, // Start the timer
  PLATFORM_TIMER_OP_READ, // Read the value of timer
  PLATFORM_TIMER_OP_SET_CLOCK, // Set the clock of the timer
  PLATFORM_TIMER_OP_GET_CLOCK, // Read the clock of the timer
  PLATFORM_TIMER_OP_GET_MAX_DELAY, // Get the maximum achievable delay
  PLATFORM_TIMER_OP_GET_MIN_DELAY // Get the minimum achievable delay
};
(END inc/platform.h)

=====================================================================

int platform_pwm_exists( unsigned id );
u32 platform_pwm_setup( unsigned id, u32 frequency, unsigned duty );
u32 platform_pwm_op( unsigned id, int op, u32 data );

TYPE: optional
USED BY MODULE: pwm

PURPOSE: PWM operations. eLua defines 16 "virtual" PWM blocks. The function
platform_pwm_exists() gets an identifier from 0 to 15 and returns 1 if the PWM
block with the given identifier exists on the target machinem, 0 otherwise.
platform_pwm_setup() is called to configure the SPI interface with the given
frequency and duty cycle (the duty cycle is a number from 0 to 100 representing
the duty cycle in percents).
Finally, platform_pwm_op() implements PWM specific operations. They are all
defined in an enum from inc/platform.h, shown below:

(BEGIN inc/platform.h)
// PWM operations
enum
{
  PLATFORM_PWM_OP_START, // Start the PWM block
  PLATFORM_PWM_OP_STOP, // Stop the PWM block
  PLATFORM_PWM_OP_SET_CLOCK, // Set the base clock of the PWM block
  PLATFORM_PWM_OP_GET_CLOCK // Get the base clock of the PWM block
};
(END inc/platform.h)

=====================================================================

void platform_cpu_enable_interrupts();
void platform_cpu_disable_interrupts();
u32 platform_cpu_get_frequency();

TYPE: optional
USED BY MODULE: cpu

PURPOSE: CPU interfacing. It allows the user to control some of the CPU functions
directly from Lua. platform_cpu_enable_interrupts() enables the CPU interrupts
(globally), while platform_cpu_disable_interrupts() disables them.
platform_cpu_get_frequency() returns the CPU "core" frequency in Hz.

=====================================================================

void platform_eth_send_packet( const void* src, u32 size );
u32 platform_eth_get_packet_nb( void* buf, u32 maxlen );
void platform_eth_force_interrupt();
u32 platform_eth_get_elapsed_time();

TYPE: optional
USED BY MODULE: net, also used by the generic TCP/IP support

PURPOSE: network support. These functions are used by uIP (the TCP/IP stack of
eLua) to implement TCP/IP services on top of the Ethernet ones (for platforms
that have an integrated Ethernet controller, or are using an external Ethernet
controller).
platform_eth_send_packet() sends the packet pointed by "src" with size "size"
over the network.
platform_eth_get_packet_nb() reads an Ethernet packet in "buf", without
exceeding "maxlen" of data. If an Ethernet packet is not available when this
function is called, it returns 0 immediately (non-blocking receive), otherwise
it returns a negative integer if the packet size is too large or the length of
the packet if it fits in "maxlen" bytes.
platform_eth_force_interrupt() is used to force an Ethernet receive interrupt.
This is needed because uIP's processing function is called from this Ethernet
interrupt handler alone.
platform_eth_get_elapsed_time() will return the approximate time (in ms) that
passed since the last call to platform_eth_get_elapsed_time(). It is used by uIP
to process periodic events.

For an example of how these functions should be implemented, take a look at the
LM3S backend (src/platform/lm3s/platform.c)
eLua platform modules
=====================================================================

(NOTE: after reading this, check also the "generic_modules.txt" file to
learn about the generic (not platform specific) modules from eLua).

In order to make eLua usable on different platform, eLua provides a number of
"platform modules" that link the language with the hardware platform. They're
mainly tied up with the platform peripherals (PIO, UART, SPI and others).
They are loaded when Lua starts (just like the "standard" modules like os, math,
string).

All the platform modules have two parts: the generic part (the one that is
exposed directly to Lua and it's supposed to be platform independent) and the
platform specific part (the one that links the module operations to actual
hardware operations). Consequently, when adding a new platform, one doesn't need
to rewrite the whole module, just the platform-dependent part. The "platform
interface.txt" file shows the conenction between platform modules and platform
interface functions. For example, the "pio" module (src/modules/pio.c) needs 3
functions for interfacing with a specific platform: platform_pio_has_port,
platform_pio_has_pin and platform_pio_op.

All the modules are located in the "src/modules" directory. Besides their
actual implementation, the "src/modules/auxmods.h" file contains the Lua
compatible description of all the modules in the system.

Sometimes it doesn't make sense to include all the modules for a particular
platform. For example, for the i386 platform it doesn't make sense to include
the "pio" module (although this is technically possible by providing "bogus"
platform interface functions, the module won't be able to do anything on a i386
CPU, unless you want to "emulate" it via the parallel port or some other
peripheral). To accomodate this, each platform must provide a "platform_conf.h"
(src/platform/<your platform>) which (amongst other things) lists the modules
that are used for that specific platform. For example, if we want to enable
only the PIO module for the AT91SAM7X platform, the "platform_conf.h" file
would look like this:

(BEGIN src/platform/at91sam7x/platform_conf.h)
// Auxiliary libraries that will be compiled for this platform

#ifndef __PLATFORM_CONF_H__
#define __PLATFORM_CONF_H__

#include "auxmods.h"

...............................................................

#define LUA_PLATFORM_LIBS\
  { AUXLIB_PIO, luaopen_pio }

#endif
(END src/platform/at91sam7x/platform_conf.h)

On the other hand, for a platform that doesn't need to enable any modules at
all, you don't even need to define the LUA_PLATFORM_LIBS macro.
This is why some of platform functions described in "platform interface.txt" are
optional. If there are no modules that use them in one platform, then you don't
need to define them at all for that platform, not even as "bogus" functions.

=====================================================================
=== The PIO module
=====================================================================

The PIO module lets Lua access the programmable input/output (PIO) pins of the
microcontroller. It exposes symbolic name for ports (pio.PA, pio.PB, ... pio.PF)
and symbolic names for port pins (pio.PA_0, pio.PA_1, ... pio.PB_30, ...). Also,
it exposes functions to access both ports and pins:

pio.setpin( value, Pin1, Pin2 ... ): set the value to all the pins in the list
  to "value" (0 or 1).

pio.set( Pin1, Pin2, ... ): set the value of all the pins in the list to 1.

Val1, Val2, ... = pio.get( Pin1, Pin2, ... ): reads one or more pins and returns
  their values (0 or 1).

pio.clear( Pin1, Pin2, ... ): set the value of all the pins in the list to 0.

pio.input( Pin1, Pin2, ... ): set the specified pin(s) as input(s).

pio.output( Pin1, Pin2, ... ): set the specified pin(s) as output(s).

pio.setport( value, Port1, Port2, ... ): set the value of all the ports in the
  list to "value".

Val1, Val2, ... = pio.getport( Port1, Port2, ... ): reads one or more ports and
  returns their values.

pio.port_input( Port1, Port2, ... ): set the specified port(s) as input(s).

pio.port_output( Port1, Port2, ... ): set the specified port(s) as output(s).

pio.pullup( Pin1, Pin2, ... ): enable internal pullups on the specified pins.
Note that some CPUs might not provide this feature.

pio.pulldown( Pin1, Pin2, ... ): enable internal pulldowns on the specified
pins. Note that some CPUs might not provide this feature.

pio.nopull( Pin1, Pin2, ... ): disable the pullups/pulldowns on the specified
pins. Note that some CPUs might not provide this feature.

Port = pio.port( code ): return the physical port number associated with the
given code. For example, "pio.port( pio.P0_20 )" will return 0.

Pin = pio.pin( code ): return the physical port number associated with the
given code. For example, "pio.pin( pio.P0_20 )" will return 20.

=====================================================================
=== The SPI module
=====================================================================

The SPI module lets Lua access the SPI interfaces of the target CPU. It exposes
functions for SPI setup and sending/receiving data, selecting/unselecting slave
devices, as well as different SPI specific constants.

Actual_clock = spi.setup( id, spi.MASTER | spi.SLAVE, clock, cpol, cpha,
  databits): set the SPI interface with the given parameters, returns the clock
  that was set for the interface.

spi.select( id ): sets the SS line of the given interface.

spi.unselect( id ): clears the SS line of the given interface.

spi.send( id, Data1, Data2, ... ): sends all the data to the specified SPI
  interface.

In1, In2, ... = spi.send_recv( id, Out1, Out2, ... ): sends all the "out" bytes
  to the specified SPI interface and returts the data read after each sent byte.

=====================================================================
=== The UART module
=====================================================================

The UART module lets Lua access the UART interfaces of the target CPU. It
exposes functions for UART setup and sending/receiving data, as well as some
UART specific constants.

Actual_baud = uart.setup( id, baud, databits,
  uart.PAR_EVEN |uart.PAR_ODD | uart.PAR_NONE,
  uart.STOP_1 | uart.SSTOP_1_5 | uart.STOP_2 ): set the UART interface with the
  given parameters, returns the baud rate that was set for the UART.

uart.send( id, Data1, Data2, ... ): send all the data to the specified UART
  interface.

Data = uart.recv( id, uart.NO_TIMEOUT | uart.INF_TIMEOUT | timeout ): reads a
  byte from the specified UART interface.

uart.sendstr( id, str1, str2, ... ): this is similar to "uart.send", but its
  parameters are string.

=====================================================================
=== The timer module
=====================================================================

It allows Lua to execute timer specific operations (delay, read timer value,
start timer, get time difference).

tmr.delay( id, delay ): uses timer 'id' to wait for 'delay' us.

Data = tmr.read( id ): reads the value of timer 'id'. The returned value is
  platform dependent.

Data = tmr.start( id ): start the timer 'id', and also returns its value at
  the moment of start. The returned value is platform dependent.

diff = tmr.diff( id, end, start ): returns the time difference (in us) between
  the timer values 'end' and 'start' (obtained from calling tmr.start or
  tmr.read). The order of end/start is irrelevant.

Data = tmr.mindelay( id ): returns the minimum delay (in us ) that can be
  achieved by calling the tmr.delay function. If the return value is 0, the
  platform layer is capable of executing sub-microsecond delays.

Data = tmr.maxdelay( id ): returns the maximum delay (in us) that can be
  achieved by calling the tmr.delay function.

Data = tmr.setclock( id, clock ): sets the clock of the given timer. Returns the
  actual clock set for the timer.

Data = tmr.getclock( id ): return the clock of the given timer.

=====================================================================
=== The platform data module
=====================================================================
It allows Lua to identify the platform on which it runs.

Platform = pd.platform(): returns the platform name (f.e. LM3S)

Cpu = pd.cpu(): returns the CPU name (f.e. LM3S8962)

Board = pd.board(): returns the CPU board (f.e. EK-LM3S8962)

=====================================================================
=== The PWM module
=====================================================================

It allows Lua to use the PWM blocks on the target CPU.

Data = pwm.setup( id, frequency, duty ): sets the PWM block 'id' to generate the
  specified frequency with the specified duty cycle (duty is an integer number
  from 0 to 100, specifying the duty cycle in percents). It returns the actual
  frequency set on the PWM block.

pwm.start( id ): start the PWM block 'id'.

pwm.stop( id ): stop the PWM block 'id'.

Data = pwm.setclock( id, clock ): set the base clock of the PWM block 'id' to
  the given clock. In returns the actual clock set on the PWM block.

Data = pwm.getclock( id ): returns the base clock of the PWM block 'id'.

=====================================================================
=== The CPU module
=====================================================================

It brings low level CPU access to Lua (read/write memory, enable/disable
interrupts).

w32( address, data ) : write the 32-bit data at the specified address

w16( address, data ) : write the 16-bit data at the specified address

w8( address, data ) : write the 8-bit data at the specified address

Data = r32( address ) : reads 32-bit data from the specified address

Data = r16( address ) : reads 16-bit data from the specified address

Data = r8( address ) : reads 8-bit data from the specified address

cli(): disable CPU interrupts

sei(): enable CPU interrupts

Clock = clock(): returns the CPU frequency

Also, you can expose as many CPU constants (for example memory mapped registers)
as you want to this module. You might want to use this feature to access some
CPU memory areas (as defined in the CPU header files from the CPU support
package) directly from Lua. To do this, you'll need to define the
PLATFORM_CPU_CONSTANTS macro in the platform's platform_conf.h file
(src/platform/<platform name>/platform_conf.h). Include all your constants in a
_C( <constant name> ) definition, and then build your project.
For example, let's suppose that your CPU's interrupt controler has 3 memory
mapped registers: INT_REG_ENABLE, INT_REG_DISABLE and INT_REG_MASK. If you want
to access them from Lua, locate the header that defines the values of these
registers (I'll assume its name is "cpu.h") and add these lines to the
platform_conf.h:

#include "cpu.h"

#define PLATFORM_CPU_CONSTANTS\
  _C( INT_REG_ENABLE ),\
  _C( INT_REG_DISABLE ),\
  _C( INT_REG_MASK )

After this you'll be able to access the regs directly from Lua, like this:

data = cpu.r32( cpu.INT_REG_ENABLE )
cpu.w32( cpu.INT_REG_ENABLE, data )

For a "real-life" example, see the src/platform/lm3s/platform_conf.h file.
TCP/IP in eLua
=====================================================================

eLua's TCP/IP support was designed with flexibility and ease of use in mind. It
might not provide all the functions of a "full-fledged" TCP/IP stack, but it's
still fully functional and probably easier to use than a "regular" (POSIX) TCP/IP
stack. These are the services provided by the TCP/IP stack:

- a set of functions for network access (defined in inc/elua_net.h)
- a DHCP client
- a DNS resolver
- a module ("net") which can be used from Lua to access the network functions
- a Telnet miniclient, which is used to support the eLua shell via TCP/IP instead
  of serial connections.

For more details about the networking API, consult docs/generic_modules.txt.

TCP/IP configuration
=====================================================================

To configure the TCP/IP subsystem, edit src/platform/[platform]/platform_conf.h
and:

1. #define BUILD_UIP to enable TCP/IP support
2. if you'll be using the DHCP client, just #define BUILD_DHCPC to build the
   DHCP client. In any case, you must also define a static network configuration:

  #define ELUA_CONF_IPADDR0 ... ELUA_CONF_IPADDR3 : the IP address
  #define ELUA_CONF_NETMASK0 ... ELUA_CONF_NETMASK3 : the network mask
  #define ELUA_CONF_DEFGW0 ... ELUA_CONF_DEFGW3 : the default gateway
  #define ELUA_CONF_DNS0 ... ELUA_CONF_DNS3 : the DNS server

  Note that you must define both BUILD_DHCPC and the ELUA_CONF_* macros. If the
  DHCP client fails to obtain a valid IP address, the static configuration will
  be used instead. To use only the static configuration (and make the eLua image
  size a bit smaller) don't define the BUILD_DHCPC client.

3. #define BUILD_DNS if you want support for the DNS server.
4. #define BUILD_CON_TCP if you want support for shell over telnet instead of
   serial. Note that you must NOT define BUILD_CON_GENERIC in this case.

TCP/IP implementation internals
=====================================================================
The TCP/IP support was designed in such a way that it doesn't require a specific
TCP/IP stack implementation. To work with eLua, a TCP/IP stack must simply
implement all the functions defined in the inc/elua_net.h file. This allows for
easy integration of more than one TCP/IP stack. Currently only uIP is used in
eLua, but lwIP (and possibly others) are planned to be added at some point.
Another key point of the TCP/IP implementation (and of the whole eLua design
for that matter) is that it should be as platform independent as possible: write
everything in a platform-independent manner, except for some functions (as few as
possible and as simple as possible) that must be implemented by each platform).
To illustrate the above, a short overview of the uIP integration is given below.

uIP in eLua
=====================================================================

uIP (http://www.sics.se/~adam/uip/index.php/Main_Page) is a minimalistic TCP/IP
stack designed specifically for resource constrained embedded systems. While the
design and implementation of uIP are an excellent example of what can be done
with a few kilobytes of memory, it has a number of quirks that make it hard to
integrate with eLua. First, it uses a callback approach, as opposed to the
sequential approach of "regular" TCP/IP stacks. It provides a "protosocket"
library that can be used to write uIP applications in a more "traditional" way,
but it's quite restrictive. So, to use it with eLua, a translation layer was
needed. It is implemented in src/elua_uip.c, and its sole purpose is to "adapt"
the uIP stack to the eLua model: implement the functions in inc/elua_net.h and
you're ready to use the stack. In this case the "adaption layer" is quite large
because of uIP's callback-based design.
To make the uIP implementation as platform-independent as possible, a special
networking layer is added to the platform interface (docs/platform_interface.txt
for details). There are only 4 functions that must be implemented by a backend
to use the networking layer. They might change as more TCP/IP stacks are added
to eLua, but probably the networking layer won't get much bigger than it is now.

For a more in-depth understanding of how the networking layer is implemented,
look at the LM3S implementation in src/platform/lm3s/platform.c.
Terminal support in eLua
=====================================================================

NOTE: currently, this only works over serial connections (not over TCP/IP)

Besides standard stdio/stdout/stderr support (docs/console_input_output.txt),
eLua provides the "term" module to access ANSI compatible terminal emulators.
It is designed to be as flexible as possible, thus allowing a large number of
terminal emulators to be used.
To use the term module, remember to:

- build it (add BUILD_TERM in your build.h file)
- build its Lua binding ( add AUXLIB_TERM in your platform_libs.h)

See docs/elua_components.h and docs/platform_modules.txt for details.

To use it, first call the "term_init" function:

(BEGIN inc/term.h)
...........................
// Terminal output function
typedef void ( *p_term_out )( u8 );
// Terminal input function
typedef int ( *p_term_in )( int );
// Terminal translate input function
typedef int ( *p_term_translate )( u8 );
...........................
// Terminal initialization
void term_init( unsigned lines, unsigned cols, p_term_out term_out_func,
        p_term_in term_in_func, p_term_translate term_translate_func );
(END inc/term.h)

The initialization function gets the physical size of the terminal emulator
window (usually 80 lines and 25 cols) and three function pointers:

- p_term_out: this function will be called to output characters to the terminal.
  It receives the character to output as its single parameter.
- p_term_in: this function will be called to read a character from the terminal.
  It receives a parameter that can be either TERM_INPUT_DONT_WAIT (in which case
  the function returns -1 immediately if no character is available) or
  TERM_INPUT_WAIT (in which case the function will wait for the character).
- p_term_translate: this function translates terminal-specific codes to "term"
  codes. The "term" codes are defined in an enum from inc/term.h:

(BEGIN inc/term.h)
...........................
  _D( KC_UP ),\
  _D( KC_DOWN ),\
  _D( KC_LEFT ),\
...........................
  _D( KC_ESC ),\
  _D( KC_UNKNOWN )
...........................
(END inc/term.h)

By using this function, it is possible to adapt a very large number of "term
emulators" to eLua. For example, you might want to run eLua in a "standalone
mode" that does not require a PC at all, just an external LCD display and maybe
a keyboard for data input. Your eLua board can connect to this standalone
terminal using its I/O pins, for example via SPI. By writing the three functions
described above, the effort of making eLua work with this new type of device is
minimal, as writing an "ANSI emulation" for your terminal device is not hard.
For an example, see src/main.c, where these functions are implemented for an
UART connection with a terminal emulator program running on PC.
To see what functions are exported to eLua by the "term" module reffer to the
"generic_modules.txt" file from the docs/ directory.
The eLua shell
=====================================================================
After you burn eLua to your board and you connect the board to your terminal
emulator running on the PC, you'll be greeted with the eLua shell prompt, which
allows you to:

- run 'lua' as you would run it from the Linux or Windows command prompt
- upload a Lua source file via XMODEM and execute in on board
- query the eLua version
- get help on shell usage

To enable the shell, define BUILD_SHELL in your build.h file, and also
BUILD_XMODEM if you want to use the "recv" command (see below). See
docs/elua_components.txt for more details about enabling the shell.

You'll need to configure your terminal emulation program to connect to your eLua
board. These are the parameters you'll need to set for your serial connection:

- speed 115200, 8N1 (8 data bits, no parity, one stop bit)
- no flow control
- newline handling (if available): CR on receive, CR+LF on send

After you setup your terminal program, press the RESET button on the bord.
When you see the "eLua# " prompt, just enter "help" to see the on-line shell
help:

eLua# help
Shell commands:
  help - print this help
  lua [args] - run Lua with the given arguments
  recv - receive a file (XMODEM) and execute it
  ver - print eLua version
  exit - exit from this shelll

More details about some of the shell commands are presented below.

The "recv" command
=====================================================================
To use this, your eLua target image must be built with support for XMODEM (see
docs/elua_components.txt for details). Also, your terminal emulation program must
support sending files via the XMODEM protocol. Both XMODEM with checksum (the
original version) and XMODEM with CRC are supported, but only XMODEM with 128
byte packets is allowed (XMODEM with 1K packets won't work).
To use this feature, enter "recv" at the shell prompt. eLua will respond with
"Waiting for file ...". At this point you can send the file to the eLua board
via XMODEM. eLua will receive and execute the file. Don't worry when you see 'C'
characters suddenly appearing on your terminal after you enter this command,
this is how the XMODEM transfer is initiated.

The "lua" command
=====================================================================
This allows you to start the Lua interpreter with command line parameters, just
as you would do from a Linux or Windows command prompt. This command has some
restrictions:

- the command line can't be longer than 50 chars
- character escaping is not implemented. For example, the next command won't work
  because of the \' escape sequences:

eLua# lua -e 'print(\'Hello, World!\')' -i
Press CTRL+Z to exit Lua
lua: (command line):1: unexpected symbol near '\'

However, if you use both '' and "" for string quoting, it will work:

eLua# lua -e 'print("Hello, World")' -i
Press CTRL+Z to exit Lua
Lua 5.1.4 Copyright (C) 1994-2008 Lua.org, PUC-Rio
Hello,World
>
The ROM file system
=====================================================================

This is a small, read-only file system built inside eLua. It is integrated with
Newlib, so you can use standard POSIX calls (fopen/fread/fwrite...) to access
it. It is also accessible directly from Lua. The files in the file system are
part of the eLua binary image, thus they can't be modified after the image is
built. For the seame reason, you can't add/delete files after the image is built.
To use this file system:

- copy all the files you need to the romfs/ directory.
- Build eLua (docs/building.txt). As part of the build process, "mkfs.py" will
  be called, which will read the contents of the "romfs/" directory and will
  output a file that contains a binary description of the file system.
- burn your image to the target
- from your code, whenever you want to access a file, prefix its name with
  "/rom/". For example, if you want to open the "a.txt" file, you should call
  fopen like this:

  f = fopen( "/rom/a.txt", "rb" )

  If you want to execute one file from the ROM file system with Lua, simply do
  this from the shell:

  eLua# lua /rom/bisect.lua

  Or directly from Lua:

  > dofile "/rom/bisect.lua"

The maximum file name of a ROMFS file is 14 characters, including the dot
between the file name and its extension. Make sure that the file names from
romfs/ follow this rule.

Adding a new platform to eLua
=====================================================================

If you want to add a new platform to eLua, the first thing you need to check is
if the platform has enough resources to run Lua. Roughly speaking, 256k of Flash
(or even 128k for the integer-only version) and 64k of RAM should be enough for
a 32-bit platform. As usual, the more, the better (this is especially true for
the RAM memory).
Next, check if a GCC/Newlib toolchain is available for the platform. To be more
precise, the compiler doesn't really matter, as long as you're able to compile
Newlib with it. If you don't, you won't be able to compile eLua. This limitation
might be eliminated in future versions, but it's not a priority of the project,
so don't count on it happening too soon.
After this, you need to make sure that you have a basic understanding of the
platform, or at least of its initialization sequence. Most platforms require
specific sequences for initializing the clock subsystem, or for disabling the
watchdog timer, or for remapping the internal memory, and many others.
Fortunately the vast majority of chips manufacturers provide support packages
for their CPUs, so once you download the support package and understand the
initialization code, you should be safe. At the very least, you'll need:

- a "startup" sequence, generally written in assembler, that does very low level
  intialization, sets the stack pointer, zeroes the BSS section, copies ROM to
  RAM for the DATA section, and then jumps to main.
- a linker command file for GNU LD.
- the "high-level" initialization code (for example peripheral initialization).

Let's suppose that your new platform is called "foo". In order to compile eLua
for foo, follow these steps:

1. create the src/platform/foo directory
2. modify the SConstruct file from the base directory to make it aware of your
   new CPU, platform and board(s). A "board" translates into a simple macro
   definition at compile time, and makes it easy to adapt your platform code for
   different situations. For example, you might have 2 boards with the same CPU,
   but different I/O pin assignments. By checking the value of the "ELUA_BOARD"
   macro in your code you can adapt it for each board.
3. you need at least 4 files (besides your platform specific files) in the
   src/platform/foo directory:

  - conf.py: this is read by SConstruct and describes how to build files for
    the platform, as well as the platform specific files. Start from an existent
    conf.py file and modify it to suit your needs, it's easier this way.
  - type.h: data types used by eLua, declared in a platform independent way.
    Again, start from an existent type.h file and modify it if needed.
  - platform_conf.h: see "platform modules.txt", "elua_components.txt" and
    "tcpip_in_elua.txt" for details

4. implement the platform interface functions (see "platform interface.txt"). By
   convention, they should be implemented in a file called "platform.c". Note that
   SConstruct defines 3 macros that might prove useful: ELUA_CPU, ELUA_PLATFORM
   and ELUA_BOARD.

5. That's it! Build (see "building.txt") and enjoy!
=====================================================================
Building eLua
=====================================================================
Before you start, you might want to check if the list of platform modules and
eLua components are set according to your needs. See docs/platform_modules.txt
and docs/elua_components.txt for details.

To build eLua you'll need:

- a GCC/Newlib toolchain for your target (see http://elua.berlios.de for
  instructions on how to build your own toolchain). Please note that even if
  you already have a compiled toolchain, the differences in the Newlib configure
  flags (mainly the --disable-newlib-supplied-syscalls flags) might prevent
  eLua for building properly on your machine.
- Linux. Compiling under windows should be possible, however this isn't tested.
  I'm using Ubuntu, so I'm also using "apt-get". If you're using a distro with a
  different package manager you'll need to translate the "apt-get" calls to your
  specific distribution.
- python. It should be already installed; if it's not:

  $ sudo apt-get install python

- scons. eLua uses scons instead of make and makefiles, because I find scons
  much more "natural" and easier to use than make. To install it:

  $ sudo apt-get install scons

- your toolchain's "bin" directory (this is generally something like
  /usr/local/cross-arm/bin, where /usr/local/cross-arm is the directory in which
  you installed your toolchain) must be in $PATH.
- if you're building for the i386 platform, you'll also need "nasm":

  $ sudo apt-get install nasm

For each platform, eLua assumes a certain name for the compiler/linker/assembler
executable files, as shown below.

============================================================================
| Tool | Compiler | Linker | Assembler |
|------------|---------------------|----------------------|--------------------|
| Platform | | | |
|============|=====================|======================|====================|
| ARM (all) | arm-elf-gcc | arm-elf-gcc | arm-elf-gcc |
|============|=====================|======================|====================|
| i386 | i686-elf-gcc | i686-elf-gcc | nasm |
|============|=====================|======================|====================|
| Cortex-M3 | arm-elf-gcc | arm-elf-gcc | arm-elf-gcc |
|============|=====================|======================|====================|

If your toolchain uses different names, you have to modify the "conf.py" file
from src/platform/[your platform].

To build, go to the directory where you unpacked your eLua distribution and
invoke scons:

$ scons [target=lua | lualong]
  [cpu=at91sam7x256 | at91sam7x512 | i386 | str912fw44 | lm3s8962 |
        lm3s6965 | lpc2888 | str711fr2 ]
  [board=ek-lm3s8962 | ek-lm3s6965 | str9-comstick | sam7-ex256 | lpc-h2888 |
        | mod711 | pc]
  [cpumode=arm | thumb]
  [allocator = newlib | multiple]
  [prog]

Your build target is specified by two paramters: cpu and board. "cpu" gives the
name of your CPU, and "board" the name of the board. A board can be associated
with more than one CPU. This allows the build system to be very flexible. You
can use these two options together or separately, as shown below:

- cpu=name: build for the specified CPU. A board name will be assigned by the
  build system automatically.
- board=name: build for the specified board. The CPU name will be inferred by
  the build system automatically.
- cpu=name board=name: build for the specified board and CPU.

For board/CPU assignment look at the beginning of the SConstruct file from the
base directory, it's self-explanatory.

The other options are as follows:

- target=lua | lualong: specify if you want to build full Lua (with floating
  point support) or integer only Lua (lualong). The default is "lua".
- cpumode=arm | thumb: for ARM target (not Cortex) this specifies the
  compilation mode. Its default value is 'thumb' for AT91SAM7X targets and
  'arm' for STR9 and LPC2888 targets.
- allocator = newlib | multiple: choose between the default newlib allocator
  (newlib) and the multiple memory spaces allocator (multiple). You should
  use the 'multiple' allocator only if you need to support multiple memory
  spaces, as it's larger that the default Newlib allocator (newlib). For more
  information about this reffer to platform_interface.txt. The default value
  is 'newlib' for all CPUs except 'lpc2888', since my lpc-h2888 comes with
  external SDRAM memory and thus it's an ideal target for 'multiple'.
- prog: by default, the above 'scons' command will build only the 'elf' file.
  Specify "prog" to build also the platform-specific programming file where
  appropriate (for example, on a AT91SAM7X256 this results in a .bin file that
  can be programmed in the CPU).

The output will be a file named elua_[target]_[cpu].elf (and also another
file with the same name but ending in .bin if "prog" was specified for platforms
that need .bin files for programming).
If you want the equivalent of a "make clean", invoke "scons" as shown above,
but add a "-c" at the end of the command line. "scons -c" is also recommended
after you change the list of modules/components to build for your target (see
section "prerequisites" of this document), as scons seems to "overlook" the
changes to these files on some occasions.

A few examples:

$ scons cpu=at91sam7x256

Build eLua for the AT91SAM7X256 CPU. The board name is detected as sam7-ex256.

$ scons board=sam7-ex256

Build eLua for the SAM7-EX256 board. The CPU is detected as AT91SAM7X256.

$ scons board=sam7-ex256 cpu=at91sam7x512

Build eLua for the SAM7-EX256 board, but "overwrite" the default CPU. This is
useful when you'd like to see how the specified board would behave with a
different CPU (in the case of the SAM7-EX256 board it's possible to switch the
on-board AT91SAM7X256 CPU for an AT91SAM7X512 which has the same pinout but
comes with more Flash/RAM memory).

$ scons cpu=lpc2888 prog

Build eLua for the lpc2888 CPU. The board name is detected as LPC-H2888. Also,
the bin file required for target programming is generated.

Cross-compiling Lua programs
=====================================================================
"Cross compilation" is the process of compiling a program on one system for a
different system. For example, the process of compiling the eLua binary image on
a PC is cross-compiling. Lua can be cross-compiled, too. By cross-compiling Lua
to bytecode on a PC and executing the resulting bytecode directly on your eLua
board you have two advantages:

- speed: the Lua interpreter on the eLua board doesn't have to compile your Lua
  source code, it just executes the compiled bytecode
- memory: this is more important. If you're exectuing bytecode directly, no more
  memory is "wasted" on the eLua board for compiling the Lua code to bytecode.
  Many times this could be a "life saver". If you're trying to run Lua code
  directly on your board and you're getting "not enough memory" errors, you
  might be able to overcome this by compiling the Lua program on the PC and
  running the bytecode instead.

But for this cross-compilation to work, the two Lua targets must be compatible
(they should have the same data types, with the same size, and the same memory
representation). This isn't completely true for Intel and ARM targets, as gcc
for ARM uses a very specific representation for double numbers (called FPA
format) by default, which makes bytecode files generated on the PC useless on
ARM boards. To overcome this, a "Lua cross-compilation" patch was posted on the
Lua mailing list a while ago, and it was further modified as part of the eLua
project to work with ARM targets. This is how to use it (the following
instructions were tested on Linux, not Windows, but they should work on Windows
too with little or no tweaking):

- first, make sure that your PC has already a build system intalled (gcc,
  binutils, libc, headers...). You'll also need "scons". The good news is that
  you should have it already installed, since otherwise you won't be able to
  build even regular eLua.

- from the eLua base directory, issue this command:

  $ scons -f cross-lua.py

  You should get a file called "luac" in the same directory after this.

- to compile your Lua code (in <source>.lua), issue this command:

  $ ./luac -s -ccn float_arm 64 -o <source>.luac <source>.lua
  if you're using "regular" (floating point) Lua, or:

  $ ./luac -s -ccn int 32 -o <source>.luac <source>.lua
  if you're using int-ony Lua.

- that's it! You can use the resulting file (<source>.luac) in two ways:

  - "recv" it (docs/the_elua_shell.txt)
  - copy it to the ROM file system (docs/the_rom_file_system.txt)